## Slide 1
Addressing Phase Noise Issues in FMCW Lidar
Taehwan Kim

## Slide 2
No tradeoff between peak power vs. resolution like pulsed lidar
  Requires longer integration for resolving smaller frequency difference
No need for fast electrical FE
Coherent RX achieves shot-noise limited detection with normal PD
Interference rejection
What are the issues when you try to extend the range, say 100m?
FMCW lidar
Target
FMCW LIDAR
Splitter
Coupler
Tunable Laser
Beat
Signal
Spectrometer
LO Path

## Slide 3
The farther the target is away, the less the phase noise of TX/RX beams are correlated (less coherent)
Even though you have infinite laser power, SNR is limited by the spectral purity of the tunable laser
Phase Noise Problem
Target
FMCW LIDAR
Splitter
Coupler
Tunable Laser
Beat
Signal
Spectrometer
LO Path
20cm
2m

## Slide 4
Photocurrent PSD from theory
  Beyond coherence range (𝜏 > 𝜏c), beating signal vanishes; it’s just Lorentzian lineshape + shot noise floor
  This is the case for both colored/white frequency noise in the laser
Phase Noise Problem
Linewidth: 10MHz
Coherence range: 4.77m
Scan time: 10us
Coherence range
Signal power
Phase noise pedestal peak
1m
20m

## Slide 5
Photocurrent PSD Beyond Coherence Range
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us

## Slide 6
Photocurrent PSD Beyond Coherence Range
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us
How can we solve phase noise problem?
  By using better spectral estimation algorithm
  By improving laser modulation hardware

## Slide 7
Photocurrent PSD Beyond Coherence Range
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us
How can we solve phase noise problem?
  By using better spectral estimation algorithm
  By improving laser modulation hardware

## Slide 8
Common belief: targets should always be within the coherence range
  Significantly constrains linewidth spec for tunable laser
Long-range Lidar is not targeting for 𝜇m-level accuracy
If we can assume there’s single scatterer, we can fit the PSD estimate to the known shape (Lorentzian + white background) to get better distance estimate than just FFT  peak-finding
  Problem of super-resolution!
  Given prior:
Detection Algorithm

## Slide 9
Procedure
  Estimate PSD from time-domain signal with FFT (periodogram)
  Then apply fitting with known Lorentzian prior
Fitting methods
  (Nonlinear) least squares estimation (LSE)
  Maximum likelihood estimation (MLE)
MLE can be better, as it can take into account the uneven estimation variance of periodogram over frequency bins
Spectral Estimation Process
For periodogram estimation, variance is bigger for bins with higher power
(just like shot-noise limited photodetectors)

## Slide 10
Target
FMCW LIDAR
Splitter
Coupler
Tunable Laser
Beat
Signal
Spectrometer
LO Path
PD
Integrate
A
Phase
mod.
20cm
2m
Phase noise!
Detector algorithm
Improved optical PLL with feedforward noise canceling

## Slide 11
Example
Distance: 20m
Linewidth: 10MHz2/Hz
Chirp bandwidth: 10GHz
Scan time: 10us
    Bin-size limited resolution: 1.5cm
100 samples
Zero shot noise
Periodogram + peak-finding
LSE
MLE
𝜎=58.7cm
𝜎=8.2cm
𝜎=6.4cm

## Slide 12
Example
Distance: 20m
Linewidth: 10MHz2/Hz
Chirp bandwidth: 40GHz
Scan time: 10us
  Bin-size limited resolution: 0.375cm
100 samples
Zero shot noise
Periodogram + peak-finding
LSE
MLE
𝜎=13.8cm
𝜎=2.03cm
𝜎=1.5cm

## Slide 13
Plugging everything into the end-to-end model, what is the required RX power to achieve desired accuracy (say 10cm)?
  Required LO power is determined by the electrical frontend design  need to increase just until the photodetector is shot-noise limited
  The performance is no longer sensitive to the distance once it’s in incoherent regime
End-to-End Model for System Design Guideline
Target
FMCW LIDAR
Splitter
Coupler
Tunable Laser
Beat
Signal
Spectrometer
LO Path
How much power we need here to hit certain accuracy target?

## Slide 14
End-to-End Model for System Design Guideline
Takeaway
  Actual spectral estimation algorithm has to be included in the system-level specification
  For given linewidth, there’s a lower bound for the required RX beam power (so that the Lorentzian is not completely buried by the shot noise floor)
  Beyond that lower bound and for target accuracy, required power is inversely proportional to the chirp bandwidth
    Chirp bandwidth: 10GHz
    Scan time: 10us
    RPD: 1A/W
    MLE fitting

## Slide 15
Photocurrent PSD Beyond Coherence Range
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us
How can we solve phase noise problem?
  By using better spectral estimation algorithm
  By improving laser modulation hardware

## Slide 16
Optical PLL for laser chirp linearization
  Can solve chirp nonlinearity problem, but phase noise filtering is limited by the closed-loop bandwidth of the PLL
Feedforward Phase Noise Cancellation

## Slide 17
Laser phase noise reduction with feedforward cancellation
  Use asymmetric MZI to measure the phase noise & actively cancel it using phase modulator
Feedforward Phase Noise Cancellation
[Aflatouni 2010]

## Slide 18
Optical PLL already has an interferometer
  Since it’s chirped, we just need to down-convert the photocurrent to the DC using an analog mixer
Feedforward Phase Noise Cancellation for FMCW Lidar
PD
Integrate
A
Phase
mod.
Final
laser out
Analog PD for removing phase ramp

## Slide 19
Simulation Result
Distance: 20m
Linewidth: 10MHz2/Hz
Scan time: 10us
Chirp bandwidth: 40GHz
MZI delay difference: 1ns

## Slide 20
Implementation Issues
PD
Integrate
A
Phase
mod.
Final
laser out
Gain/delay needs to be matched well
  Gain of FF path ∝ 𝜏
  On-chip 𝜏: a few ns at most
  Requires huge gain…
Also, removal of phase ramp using analog mixer can introduce a lot of noise
  Phase multiplication before downconverting could help

## Slide 21
Actual Demonstration Platform
FMCW Lidar prototype chip CMOS: 3x1.5mm, GF45nm SOI process
  Similar optical PLL system as Behnam’s but implemented in digital to have more flexibility so that it can be compatible with wider range of laser/photonics

## Slide 22
Actual Demonstration Platform
FMCW Lidar prototype chip photonics: CNSE 300mm process
Delay (1.14ns)
BPD (got 20uApp for 0dBm)
Lidar TX/RX
LO Path
9:1 tap