## Slide 1: Phase noise problem
As 𝜏R goes up, PN of TX/RX beams are less correlated (less coherent)
Beating tone becomes weaker & noise floor go up
[Vasilyev 2013]
20cm
2m

## Slide 2: Phase noise example
Photocurrent PSD from theory
Even without shot noise, ranging accuracy is fundamentally limited by PN
Beyond coherence length (tau>tau_c), it’s just Lorentzian lineshape + shot noise floor
Linewidth: 10MHz
Coherence range: 4.77m
Scan time: 10us
Coherence range
Signal power
Phase noise pedestal peak
1m
20m
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 3: Phase noise example
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 4: Phase noise example
Photocurrent PSD from theory
Even without shot noise, ranging accuracy is fundamentally limited by PN
Beyond coherence length (tau>tau_c), it’s just Lorentzian lineshape + shot noise floor
Linewidth: 10MHz
Coherence range: 4.77m
Scan time: 10us
Coherence range
Signal power
Phase noise pedestal peak
1m
20m
Even beyond coherence range, it is still possible to estimate the distance from Lorentzian lineshape (just less accurate)
Beyond coherence range, PSD peak height is constant (function of linewidth)
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 5: Detector for long-distance targets
Common belief: targets should always be within the coherence range
  Significantly constrains linewidth spec for tunable laser
However, if we can assume there’s single scatterer, we can fit the PSD estimate to the known shape (Lorentzian) to get better distance estimate than just (FFT  peak-finding)
  Problem of super-resolution
Lorentzian lineshape + shot noise floor
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 6: Fitting
Procedure
  Estimate PSD from time-domain signal with FFT (periodogram)
  Then apply fitting with known Lorentzian prior
Fitting methods
  (Nonlinear) least squares estimation (LSE)
  Maximum likelihood estimation (MLE)
MLE can be better, as it can take into account the uneven estimation variance of periodogram over frequency bins
For periodogram estimation, variance is bigger for bins with higher power
(just like shot-noise limited photodetectors)
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 7
Distance: 20m
Linewidth: 10MHz2/Hz
Chirp bandwidth: 10GHz
Scan time: 10us
    Bin-size limited resolution: 1.5cm
100 samples
Periodogram + peak-finding
LSE
MLE
𝜎=58.7cm
𝜎=8.2cm
𝜎=6.4cm
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 8
Distance: 20m
Linewidth: 10MHz2/Hz
Chirp bandwidth: 40GHz
Scan time: 10us
  Bin-size limited resolution: 0.375cm
100 samples
Periodogram + peak-finding
LSE
MLE
𝜎=13.8cm
𝜎=2.03cm
𝜎=1.5cm
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 9: Remaining work
Plug everything into the end-to-end model, include shot noise, and see what is the required RX power to achieve desired accuracy (say 10cm) for different:
  Distance (this is not that critical once you’re in the incoherence regime)
  Linewidth
  Chirp bandwidth
  Scan time
Derive theoretical lower bound for this fitting (Cramer-Rao lower bound)
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 10: Feedforward phase noise cancellation
Key idea
PD
Integrate
A
Phase
mod.
Final
laser out
Analog PD for removing phase ramp
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 11: Simulation result
Distance: 20m
Linewidth: 10MHz2/Hz
Scan time: 10us
Chirp bandwidth: 40GHz
MZI delay difference: 1ns

## Slide 12: Works really great in simulation, however..
Gain/delay needs to be matched quite well
Gain of FF path ~ tau (a few ns)
Requires huge gain…
Also, removal of phase ramp using analog mixer can introduce a lot of noise, especially concerning as the gain of asymmetric MZI is very small
  Maybe multiplying phase directly could help?

## Slide 15: Optical PLL for FMCW Lidar
Taehwan Kim
09/25/17

## Slide 16: Lidar
Uses light to sense the distance/velocity of the remote target
Using light as sensing medium is advantageous mainly because the wavelength is small (compared to mmWave, for example)
  Diffraction-limited system: sensing with light improves lateral resolution for given device size
  In other words, can build high-resolution sensor which is also very compact
  Integrated optics: co-existence of powerful electronics & photonic devices on a single substrate is now possible

## Slide 17: Lidar
Uses light to sense the distance/velocity of the remote target
Using light as sensing medium is advantageous mainly because the wavelength is small (compared to mmWave, for example)
  Diffraction-limited system: sensing with light improves lateral resolution for given device size
  In other words, can build high-resolution sensor which is also very compact
  Integrated optics: co-existence of powerful electronics & photonic devices on a single substrate is now possible

## Slide 18: Lidar scheme summary
Pulsed vs. FMCW
[Behroozpour 2013]
Pulsed lidar
FMCW lidar

## Slide 19: Pulsed lidar
Fundamental tradeoff between peak power vs. resolution
  tau = 1.5cm  10ps
  SNR determined by the # of photons within tau
Requires high-speed electrical FE
Geiger-mode APD required for shot-noise limited receiver
No interference rejection

## Slide 20: FMCW lidar
No tradeoff between peak power vs. resolution
  Requires longer integration for resolving smaller frequency difference
No need for fast electrical FE
Coherent RX achieves shot-noise limited detection with normal PD
Interference rejection
Requires laser with broadband, stable, continuous wavelength tuning capability & narrow linewidth

## Slide 21: Today: modulator design for FMCW lidar
Linearity of the modulation pattern
Phase noise

## Slide 22: Impact of FMCW modulator performance
1. Linearity of the modulation pattern
  Due to the nonlinearity in the laser tuning & bandwidth limit, modulation pattern could diverge from the ideal  non-constant chirp rate
  Causes frequency uncertainty in the beating tone, degrading SNR
  Some kind of feedback control which senses the chirp rate & corrects the tuning signal required
Laser Frequency
Time
Laser Frequency
Time
Δf
Δf

## Slide 23: Impact of FMCW modulator performance
2. Laser phase noise
  As 𝜏R goes up, PN of TX/RX beams are less correlated (less coherent)
  Beating tone becomes weaker & noise floor go up
[Vasilyev 2013]
20cm
2m

## Slide 24: FMCW modulation closed-loop control
How to sense the instantaneous laser chirp rate?
  Lidar  known chirp rate, find out the distance
  Laser controller  For known distance, find out the chirp rate
[Satyan 2009]
Target emulation
with known 𝜏
Photocurrent frequency indicates instantaneous chirp rate  compare with ref. to generate error signal for laser control

## Slide 25: FMCW linearization: implementation
Same system as normal PLL
  Integrator + laser + MZI-PD is equivalent to single VCO
Digital implementation to accommodate wide range of reference oscillation frequency (different chirp rates)
Triangular mod. by flipping integrator sign
CMOS
Photonics

## Slide 26: Digital OPLL Implementation
1.28GHz
128
10MHz
10MHz
(fastest)
8ps LSB
(couter)
Sub-sampling to make this run at slower fb
7b
7b
Signed 10b

## Slide 27: Digital backend functionalities
Variable reference frequency operation
  Feedback clock can be slower than nominal (10MHz) as we might want to use a laser with lower chirp rate or smaller chirping bandwidth
  However, fine TDC resolution is set by inverter delay
  By using frequency detector to introduce frequency offset, we can make the loop work with slower feedback frequency
  Error values are updated only at the fb clock positive edge (sub-sampling operation)
All-pass triangular modulation by synchronized sign flipping

## Slide 28: All-pass triangular modulation
Sign flipping – synchronized with ref. clk
When the sign is flipped, 𝜋 phase error is introduced instantaneously
(takes some time to settle, depending on loop BW)
Notes: S_{t_{q,TDC}}(e^{j\omega T_R})=\frac{\left(\Delta t_{del}\right)^2}{12}

## Slide 29: No Frequency Offset, Two Pt Mod On
By resetting the counter (coarse TDC) when the sign is flipped, we can cancel this 𝜋 phase error & hide sign flipping from the loop
Notes: S_{t_{q,TDC}}(e^{j\omega T_R})=\frac{\left(\Delta t_{del}\right)^2}{12}

## Slide 30: Noise Sources in Optical PLL
PIR control:
Proportional path : 𝛼
Integration path: 𝛽
Maximize laser noise suppression
Minimize additive noise from PLL
Minimize effective linewidth 
Notes: S_{t_{q,TDC}}(e^{j\omega T_R})=\frac{\left(\Delta t_{del}\right)^2}{12}

## Slide 31
Noise TF
Looking at the laser PSD, it is highpass  need to maximize loop bandwidth
Choose design variables accordingly so that additive noise is not exceeding laser phase noise
  TDC LSB
  LF gain
  Current DAC LSB
  Capacitance size
  Buffer gain
Notes: \frac{\phi_{out}}{\phi_{n,laser}}(s)=\frac{s^2}{s^2+\left( \frac{\tau}{2\pi} \frac{K_{laser}}{\Delta t_{del}} \frac{A_{drv}I_{LSB}}{C} \right) (\alpha s T_R + \beta)}=\frac{s^2}{s^2+\eta\alpha s T_R + \eta\beta} \frac{\phi_{out}}{t_{q,TDC}}(s)=\frac{1}{s}\frac{\frac{2\pi}{\tau}\eta (\alpha s T_R+\beta)}{s^2+\eta\alpha s T_R + \eta\beta}
S_{\phi_{out}}(f)|_{iDAC}=\frac{1}{T_R} \left| \frac{\phi_{out}}{t_{q,iDAC}}(f) \right|^2 S_{t_{q,iDAC}(e^{j\omega T_R})}
S_{\phi_{out}}(f)|_{laser}= \left| \frac{\phi_{out}}{\phi_{n,laser}}(f) \right|^2 S_{\phi_{n,laser}}(f) = 2\pi\Delta\nu \left| \frac{s}{s^2+s\frac{\omega_0}{Q} + \omega_0^2} \right|^2
S_{\phi_{out}}(f)|_{iDAC}=\frac{1}{T_R} \left| \frac{\phi_{out}}{t_{q,iDAC}}(f) \right|^2 S_{t_{q,iDAC}(e^{j\omega T_R})}=\frac{1}{12T_R} \left| \frac{\frac{2\pi}{\tau}\frac{\Delta t_{del}}{\alpha} \frac{\omega_0}{Q}}{s^2+s\frac{\omega_0}{Q} + \omega_0^2} \right|^2
S_{\phi_{out}}(f)|_{TDC}=\frac{1}{T_R} \left| \frac{\phi_{out}}{t_{q,TDC}}(f) \right|^2 S_{t_{q,TDC}(e^{j\omega T_R})}=\frac{(\Delta t_{del})^2}{12T_R} \left| \frac{1}{s} \frac{\frac{2\pi}{\tau} \eta T_R (s + \omega_z)}{s^2+ s\omega_0/Q + \omega_0^2} \right|^2

## Slide 32: Design Procedure
Maximize the loop bandwidth while ensuring stability
  The wider the bandwidth, the more the laser noise is suppressed
  Set bandwidth to be 15% of the reference clock, Q=0.5
  η and α/β determined
Now to choose α, ILSB, C
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 33: Design Procedure
Set α so that iDAC quantization noise is balanced with others
  It fixes ILSB/C ratio
Finally, increase ILSB & C until iDAC thermal noise is balanced with others
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 34: Plugging in Real Numbers
Given values:
Design parameters:
Runtime Parameters:

## Slide 35: Plugging in Real Numbers

## Slide 36: Optical PLL prototype chip (Aug.`17): 3x1.5mm

## Slide 37: Optical PLL prototype chip (Aug.`17): 3x1.5mm
Variant 1
Variant 2
(variant 1 - capacitor)
Variant 3
(variant 2 - laser buffer - TIA)
Cur. Mir.
CML2CMOS

## Slide 38: Photonics chip from EPHI (Mar.`15)
Delay (1.14ns)
BPD (got 20uApp for 0dBm)
Lidar TX/RX
LO Path
9:1 tap

## Slide 39: Optical PLL prototype chip (Aug.`17): 3x1.5mm
Capacitor
iDACs
Backend
Fine TDC chain
TIA
(DODOS)
Buffer

## Slide 40: Fine TDC
Standard inverter-chain based TDC, 8ps LSB @ 1V
128 segments -> 7bit
Capable of calibrating the normalization factor by measuring fast clock period in # of inverter delays (nominal: ~100)
Clock tree to minimize the skew
[Staszewski 2004]
Clock tree

## Slide 41: Sign generator for triangular waveform
(From pad)
(From pad)

## Slide 42: Sign generator for triangular waveform
Nandish’s StrongArm design reused
In digital backend
(From pad)
(From pad)

## Slide 43: Current DAC & capacitance
Push-pull DAC (9b)
Desiged LSB 100nA
Pulse width of sign & sign_b are slightly reduced to make sure it’s either sinking or sourcing (not both)
Reference current of sink/source DAC can be independently controlled by central current mirror (can correct current mismatch off-chip)
Cap: dgncap (3.8x4.8u*2016) ~ 3.6nF @ 0.9V
9b
9b
9b
9b

## Slide 44: Current DAC
Based on Pavan’s current mirror design

## Slide 45: Laser buffer
Roughly modeled as diode + 50Ohms in series
Dedicated current reference for biasing at 8mA
For 100GHz chirp BW, ~3mApp swing required
Designed transconductance: 20mS
Laser tuning input V/I curve
Desired bias point
(8mA, 1.27V)