## Slide 1: Addressing phase noise issues in FMCW Lidar
Taehwan Kim
10/16/17

## Slide 2: Impact of phase noise on FMCW LIDAR
As 𝜏 goes up, PN of TX/RX beams are less correlated (less coherent)
Beating tone becomes weaker & noise pedestal go up
20cm
2m
Linewidth=1MHz, T=10us
Cross @ 82m

## Slide 3: Nature of phase noise in tunable lasers
The common source of phase noise in lasers is spontaneous emission in the cavity
  White frequency noise (noise density 𝛥𝜈 (Hz2/Hz)=Linewidth)
  Coherence time (𝜏c) = 1/Linewidth, coherence length = c𝜏c
Actual laser has other noise sources
  Especially tuning function can add various noise mechanisms
Phase noise density
Frequency
MEMS mirror VCSEL
DBR laser
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 4: Phase noise example
Photocurrent PSD from theory
Even without shot noise, ranging accuracy is fundamentally limited by PN
Beyond coherence length (tau>tau_c), it’s just Lorentzian lineshape + shot noise floor
Linewidth: 10MHz
Scan time: 10us
Signal power
Phase noise pedestal peak
1m
20m
Even beyond coherence range, it is still possible to estimate the distance from Lorentzian lineshape (just less accurate)
Beyond coherence range, PSD peak height is constant (function of linewidth)
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 5: Phase noise example
1m
20m
Linewidth: 10MHz2/Hz
Linewidth: 2MHz2/Hz
1m
20m
Scan time: 10us
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 6: Phase noise problem: algorithm
Common belief: targets should always be within the coherence range
  Significantly constrains linewidth spec for tunable laser
Backend: need to solve line spectral estimation problem
  Common signal model:
  In our case, phase term is actually random, and it is known that existing estimation algorithms perform poorly in presence of strong phase noise*
A. Barbieri, D. Bolletta and G. Colavolpe, GLOBECOM '05. IEEE Global Telecommunications Conference, 2005., 2005, pp. 5 pp.-.
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 7: Phase noise problem: improved algorithm
If we can assume there’s single scatterer, we can fit the PSD estimate to the known shape (Lorentzian + white background) to get better distance estimate than just FFT  peak-finding
  Given prior:
  Signal model:
  Least-squares solution:
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 8: Phase noise problem: improved algorithm
Linewidth=1MHz, T=10us, Prx=1mW
Linewidth=1MHz, T=10us, Prx=1nW
Linewidth=10MHz, T=10us, Prx=1nW
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 9: Experimental Demonstration
~100GHz, 10us chirping using DBR laser from Ming’s lab
Nonlinearity in modulation
  Measured/Calibrated using resampling [Sandborn ‘17]
  Resampling points generated from reference arm with ~10cm path difference

## Slide 10: Experimental Demonstration
Measured chirping nonlinearity
Periods
Time-domain waveform

## Slide 11: Experimental Demonstration
Nonlinearity correction for 1.5m sample

## Slide 12: Experimental Demonstration
How close is the Lorentzian model to the actual measurement?

## Slide 13: Experimental Demonstration
Lorenztian LSE: 1.5m sample
PER: sigma = 24.8cm
LLSE: sigma = 2.27cm

## Slide 14: Experimental Demonstration
Lorenztian LSE: 2.2m sample
PER: sigma = 27.3cm
LLSE: sigma = 2.19cm

## Slide 15: End-to-end system model including algorithm
(Max range, RF bandwidth)
For 5cm accuracy target, 300m, 1GHz does not work with 10MHz linewidth
By increasing RX bandwidth, chirp BW can be increased -> better perform.
By reducing maximum range, chirp BW can be increased & more coherent
T=10us
Chirp: 5GHz
Chirp: 10GHz
Chirp: 10GHz
300m, 1GHz
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}

## Slide 16: For really long distance measurement
T=1ms
Distance=1km
Linewidth=100kHz
Chirp bandwidth=5GHz
Number of MC samples=100
If now the goal is not to find out the position of the target, but to just find out if there is something within spectral ROI, SNR constraint could be less stringent
Notes: S_i(f) = \frac{{i_0}^2}{2}\left[ \frac{{\tau}_c/(2\pi)}{1+\left(\pi f {\tau}_c \right)^2} \left\{ 1- e^{-\frac{2\tau}{{\tau}_c}} \left[ \cos(2\pi f\tau) + \frac{1}{\pi f \tau_c} \sin(2\pi f \tau) \right] \right\} \right]
\tau_c = \frac{2}{\textrm{linewidth}},\quad i_0: \textrm{nominal photocurrent amplitude},\quad \tau: \textrm{path delay}